## Slide 1
Advanced Thermal Management: Cooling of Power Electronics
A Presentation on Effective Cooling Strategies for Inverters and Converters.
Presenters
Muhammad Ibrahim & Mohammad Ahtesam
Institution & Instructor
Fast NUCES Islamabad, Campus
Instructor: Al-Bara Shalaby

## Slide 2
Why Thermal Management Matters
Power electronic devices—such as inverters and converters—are critical components in modern electrical systems. However, their operation is inevitably linked to significant heat generation.
Heat Generation Sources
Heat is primarily generated within the semiconductor devices due to switching and conduction losses. These losses scale with power density and switching frequency.
The Impact of Temperature
Inefficient cooling directly reduces performance and shortens the component's lifespan, leading to premature failure and system unreliability.
Our objective is to explore robust cooling methodologies grounded in fundamental thermodynamic principles to achieve efficient thermal dissipation.

## Slide 3
Understanding Heat Generation in Power Devices
The internal thermal load must be accurately calculated and managed to ensure safe operating temperatures. Excessive heat is the enemy of reliability.
Inverter Thermal Dissipation
IGBT Module C
High-power thermal generation
Heat Sink
Collects and dissipates heat
Heat Flow Arrows
Directed toward heat sink
IGBT Module B
Conduction and switching losses
IGBT Module A
Primary switching heat source
Primary Heat Sources
Semiconductor devices (IGBTs, MOSFETs, Diodes).
Switching losses (energy dissipated during turn-on/off).
Conduction losses (resistance during 'on' state).
Critical Effects
Increased junction temperature accelerates material degradation, leading to failure modes like wire-bond lift-off and solder fatigue.

## Slide 4
The Governing Laws of Heat Transfer
Thermal management relies on three fundamental modes of heat transfer to move energy from the semiconductor junction to the ambient environment.
Conduction
Transfer through solid materials (junction, case, heat sink) governed by Fourier’s Law.
Convection
Transfer between a surface and a moving fluid (air or liquid) described by Newton’s Law of Cooling.
Radiation
Energy emitted from hot surfaces as electromagnetic waves, significant at higher temperatures.
Newton's Law of Cooling (Convection)
Where Q is the heat transfer rate, h is the convection heat transfer coefficient, A is the surface area, and T is temperature.

## Slide 5
Spectrum of Cooling Techniques
Cooling solutions are broadly categorised based on their requirement for external power input and system complexity.
Passive Cooling
Heat sinks (finned aluminium or copper).
Natural convection and radiation.
Thermal pads or interface materials (TIMs).
Characterised by low complexity and zero operating power.
Active Cooling
Forced convection via fans.
Liquid cooling systems (water-glycol).
Advanced phase change materials (PCMs).
Offers superior thermal performance but requires external energy.
Design Considerations
Metric
Cost
Thermal Efficiency
Complexity
Passive
Low
Moderate
Low
Active (Air)
Moderate
High
Moderate
Active (Liquid)
High
Very High
High

## Slide 6
Real-World Application and Future Trends
Case Study: Electric Vehicle Inverter Cooling
EV inverters handle high power densities, making efficient cooling essential for vehicle range and charging speeds. These systems almost exclusively use direct liquid cooling with coolant channels integrated directly into the heat sink base plate.
Coolant: Water-glycol mixture.
High heat flux removal capacity.
Crucial for maintaining optimal battery and powertrain performance.
Modern Trends in Thermal Management
Nanofluids
Fluids engineered with nanoparticles (e.g., copper, silver) to significantly enhance thermal conductivity.
Immersion Cooling
Submerging components directly in dielectric liquids for maximal, uniform heat removal.
Two-Phase Cooling
Utilising the latent heat of vaporisation (e.g., in heat pipes) for highly efficient heat transfer at a constant temperature.